## Slide 1: PROCESSORS HISTORICAL EVOLUTION
INTEL & ARM comparison
Ph.D. Student: Gabriella D’Andrea
(gabriella.dandrea@graduate.univaq.it)
Advisor: Luigi Pomante
Co-Advisor: Tania Di Mascio

## Slide 2
Processors infancy – from Intel to ARM
ARM Processor
ARM Processor Architecture;
The birth of ARM processor;
From Acorn RISC Machines to Advanced RISC Machines.
ARM & INTEL historical evolution
Comparison between ARM and INTEL based on the innovations introduced in the fields of Cache, Registers, Instructions and Architecture.
Outline
Processors Historical Evolution

## Slide 3: Processors infancy – from Intel to ARM
16 registers of 4 bits each;
Instruction set contained 46 instructions
Intel 4004.
The first, 4-bit CPU
8 registers of 16 bits each;
8bit data bus.
Intel 8086.
The first 16-bit CPU
First ARM processor
1971
1979
14 registers of 32 bits each.
Intel 80386.
The first 32-bit CPU
1985
1978
60 new floating point instructions adopting the IEEE 754 floating-point standard
Intel 8086.
The floating-point coprocessor
1980
1986
CISC architecture;
Instruction set contained 48 instructions;
Intel 8008.
The first standard CPU for computers
1974
Intel 8088.
Chosen for the first IBM PC
16 bit data bus.
On-die L1 cache;
Floating-point unit
Intel 80486.
Improved processors
1989
Notes: Intel 80387  paging introduction, improved characteristics of its trigonometric functions

## Slide 4
Processors infancy – from Intel to ARM
ARM Processors
ARM Processor Architecture
The birth of ARM processor
From Acorn RISC Machines to Advanced RISC Machines
ARM & INTEL historical evolution
Comparison between ARM and INTEL based on the innovations introduced in the fields of Cache, Registers, Instructions and Architecture
Outline

## Slide 5: ARM Processor Architecture
ARM is a family of Reduced Instruction Set Computing (RISC) architectures for computer processors. The ARM allows an instruction set called “Thumb”, which comprises 32-bit instructions to 16-bits, enabling programs to be coded with much more density with respect to standard RISC instruction set.
Today many embedded products like smartphones, set-top boxes, digital television, digital cameras use ARM processors due to their cost-effectiveness and low power consumption.
What is ARM?

## Slide 6: The birth of ARM processor
  Acorn’s Advanced Research and Development section produced the Acorn RISC Machine (ARM), the first reduced instruction set computer (RISC) processor for commercial use.
Year 1983
Year 1985
  With VLSI technology ARM came up with ARM1. It has been developed by Sophie Wilson, and Steve Furber, two computer scientists from the University of Cambridge. Sophie developed the instruction set for the Arm1 and Steve worked on the chip design.
Year 1986- 1987
  The successor of the initial ARM was ARM2. It uses a Von Neumann architecture, a 32-bit data bus, a 26-bit address space, and a 3-stage pipelined (Fetch, Decode, Execute).

## Slide 7: From Acorn RISC Machines to Advanced RISC Machines
ARM starts to work on the emerging personal digital assistant (PDA) redesigning the product to be static in order to reduce the chip power dissipation.
Apple meanwhile was also entering the PDA market using ARM technology but didn’t want to base a product on Acorn IP.
In 1990 a joint venture between Acorn Computers, Apple Computer, and VLSI Technology was founded. Apple invested the cash, VLSI Technology provided the tools, and Acorn provided the 12 engineers and with that Arm was born, along with its luxury office in Cambridge.
Year 1990

## Slide 8
Processors infancy – from Intel to ARM
ARM Processor
ARM Processor Architecture
The birth of ARM processor
From Acorn RISC Machines to Advanced RISC Machines
ARM & INTEL historical evolution
Comparison between ARM and INTEL processors based on the innovations introduced in the fields of Cache, Registers, Instructions and Architecture
Outline

## Slide 9: ARM & INTEL historical evolution
ARM3
1990
ARM6
1991
Processors Timeline from 1990 to 2019

## Slide 10: ARM processors improvement
 | ARM3 | ARM6
Cache | Integrated cache | Integrated cache
Registers | Register File: 27 Registers Address Registers: 26-bit 2 Data Register: 32 bit | Register File: 37 Registers Address Registers: 32-bit 2 Data Register: 32 bit
Instructions | New memory instruction | New movement instructions
Architecture | RISC | RISC
The major goal of ARM3 and ARM6 was to improve the processor speed-up performance. A target of three times the performance of ARM2 was set.
Table 1: ARM 3/6 key changes from ARM2
ARM3 – ARM6

## Slide 11: ARM & INTEL historical evolution
ARM3
1990
1993
Intel
Pentium
ARM6
1991
Processors Timeline from 1990 to 2019

## Slide 12: Intel processors improvement
 | First version of Intel Pentium Processor
Cache | 8 KB of instruction cache 8 KB of data cache
Registers | 8 32-bit general-purpose registers 8 80-bit floating-point registers.
Instructions | First instruction set SIMD
Architecture | CISC Superscalar architecture
The major goal of this processor was to improve the performance making it twice as high as the Intel 80487 processor with the same frequency.
The original Pentium carried a now-famous floating-point flaw referred to as the "FDIV bug," which ended up costing Intel an estimated $450 million in recall cost.
Intel Pentium Processor
Notes: FDIV bug La scoperta avvenne nel dicembre del 1994, quando il professore, intento nella sua opera di ricerca, tentò di calcolare il risultato di una particolare espressione matematica (la costante di Brun); il risultato ottenuto era ben lontano da quanto si era prospettato teoricamente, anche considerando possibili errori di arrotondamento. l 30 ottobre 1994, il prof inviò una e-mail che descriveva l'errore che aveva scoperto nell'unità in virgola mobile Pentium a vari contatti, richiedendo rapporti di test per la falla sui 486-DX4, Pentium e cloni Pentium
SIMD Single Instruction stream, Multiple Data stream (SIMD) è un'architettura in cui più unità di elaborazione elaborano più flussi di dati in parallelo. Il modello SIMD è composto da un'unica unità di controllo che esegue una istruzione alla volta controllando più ALU che operano in maniera sincrona. Ad ogni passo, tutti gli elementi eseguono la stessa istruzione scalare, ma ciascuno su un dato differente. Un elaboratore basato su questo modello è anche detto Array Processor.

## Slide 13: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
ARM11
2002
Processors Timeline from 1990 to 2019

## Slide 14: ARM - SIMD Introduction
ARM11 introduces 32-bit SIMD for media processing to reach up to 2x performance for video processing. This processor introduces also an optional Vector Floating Point coprocessor for automotive/industrial controls and 3D graphics acceleration.
 | ARM11
Cache | New cache architecture: L1 cache involves separate instruction and data caches; L2 cache is off-chip.
Registers | 40 registers: 33 32-bit general purposes registers; 7 32-bit status registers.
Instructions | 2 instruction sets: 32-bit ARM with SIMD introduction; 16-bit Thumb.
Architecture | RISC.
ARM 11

## Slide 15: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM11
2002
Processors Timeline from 1990 to 2019
Notes: Intel P6 family aumento livello di parallelismo superscalar architecture. superscalar processor can execute more than one instruction during a clock cycle

## Slide 16: Intel processors improvement
The P6 family is the next generation of processors in the Pentium® line of Intel processors. These processors were developed to deliver higher performance than the Pentium family while maintaining the compatibility with all previous Intel Architecture processors.
NEW Features:
Aid in the design of energy-efficient computer systems by offering multiple low-power states such as AutoHALT, Sleep, and Deep Sleep, to conserve power during idle times;
Removes the constraint of linear instruction sequencing between the traditional “fetch” and “execute” phases;
Increase the cache size to meet higher performances required by a workstation market.
Fig.1 Diagram of P6 family elements including cache and memory interface [7]
Intel P6 family

## Slide 17: The P6 family of processors
 | Pentium Pro (Year 1995) | Pentium II (Year 1997) | Pentium II Xeon (Year 1998) | Celeron (Year 1998) | Pentium III (Year 1999) | Pentium III Xeon (Year 1999)
Cache | Level 1: 32KB; Level 2: 256KB. | Level 1: 36 KB; Level 2: 256 / 512 KB. | Level 2: Up to 2 MB cache that running at the processor speed. | Level 2: 128 KB. | Equal to Pentium II. | Level 2 : Up to 2MB; L2 Cache on-die.
Registers | 8 32-bit Registers. | No significant innovations. | No significant innovations. | No significant innovations. | New register file contained 8 128-bit registers. | No significant innovations.
Instructions | More than 400 different machine instructions. | Implementation of Intel MMX integer SIMD instruction set. | No significant innovations. | No significant innovations. | Streaming SIMD Extensions (SSE) 70 new instructions. | No significant innovations.
Architecture | CISC. | CISC. | CISC. | CISC. | CISC. | CISC.
Notes: Pentium Pro registers: 8 but First four register are used for data manipulation and next four register are used to hold address
ISA: There are Register-to-Register instructions, Register-to-Memory instructions and Memory-to-Memory instructions
Pentium II  a sigla MMX (MultiMedia eXtension) infatti indica la presenza di alcune istruzioni macchina aggiuntive di tipo SIMD (Single Instruction Multiple Data). Le istruzioni SIMD applicano la stessa operazione (che può essere ad esempio una somma, o una moltiplicazione) a più dati simultaneamente (8 numeri interi da 8 bit ciascuno, oppure 4 numeri interi da 16 bit ciascuno, o ancora 2 numeri interi da 32 bit ciascuno).
Per semplificare la progettazione gli ingegneri Intel decisero di preservare la vecchia architettura alla quale venne aggiunta l'unità MMX che operava tramite un cambio di contesto del processore. L'unità MMX utilizza i registri IA-32 della FPU. Questa infelice scelta progettuale impediva di utilizzare istruzioni in virgola mobile e istruzioni MMX contemporaneamente.
Pentium II Xeon--> processor speed: Up to 450 MHz.
Intel Celeron  focus on PC market
Pentium III  three categories: Instruction SSE Streaming SIMD Extensions per sopperire al problema dell’MMX Poiché SSE aggiunge il supporto per la virgola mobile, fu molto più utilizzato di MMX dato che tutte le schede video gestiscono internamente i calcoli sui numeri interi. L'intero set era costituito da 70 istruzioni.

## Slide 18: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM11
2002
Processors Timeline from 1990 to 2019
Intel Pentium M
2003

## Slide 19: The Mobile processor
 | ARM7 - ARMI7DI
Cache | New cache architecture: L1 cache involves separate instruction and data caches; L2 cache is off-chip.
Registers | 37 registers: 31 32-bit general purposes registers; 6 32-bit status registers.
Instructions | 2 instruction sets: 32-bit ARM; 16-bit Thumb; 60 MIPS @ 59.8 MHz
Architecture | RISC.
 | Intel Pentium M - IA-32 Intel mobile processors
Cache | L1: 32 KB; L2: 1MB.
Registers | No significant innovations.
Instructions | SSE instructions; Support to SSE2 instructions.
Architecture | CISC.
ARM7TDMI was the first ARM-powered GSM phone. It was designed
for the Nokia 6110. This led to the popular series of Nokia phones using the processor, including the 3210 and 3310.
Notes: IA-32 Intel mobile processors desktop market
ARM7 JTAG based on-chip debugging

## Slide 20: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM9
1998
Intel Pentium 4
2000
ARM11
2002
Processors Timeline from 1990 to 2019
Intel Pentium M
2003

## Slide 21: The new architecture introduction
 | ARM9
Cache | Equal to ARM7.
Registers | Equal to ARM7.
Instructions | 200 MIPS @ 180 MHz;
Architecture | RISC; Harvard architecture .
 | Intel Pentium 4 processor family
Cache | Equal to Pentium M.
Registers | No significant innovations.
Instructions | 64-bit Instructions set; SSE3 instructions set.
Architecture | CISC; NetBurst microarchitecture: improve performance primarily by increasing CPU frequency.
  Intel ships updated versions of its Xeon and Pentium 4 processor families supporting the new 64-bit instruction set introduced by AMD in 1999. Intel indeed admits it has been developing a clone of the AMD64 extensions named IA-32e (later renamed EM64T, then yet again renamed to Intel 64).
Year 2004

## Slide 22: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM9
1998
Intel Pentium 4
2000
Intel Pentium M
2003
ARM11
2002
ARM
Cortex – M3
2004
Intel Quark
2013
Processors Timeline from 1990 to 2019

## Slide 23: Microcontroller cores
 | Cortex-M3
Cache | Not present (Introduced in Cortex-M7).
Registers | No significant innovations.
Instructions | Thumb-1 and Thumb-2 instruction sets; No ARM instruction sets support;
Architecture | RISC; Harvard architecture .
 | Intel Quark
Cache | L2: 16KB.
Registers | No significant innovations.
Instructions | Equal to Pentium M; No SMID support ; Support to embedded operating systems .
Architecture | CISC.
Notes: microcontrollers, ASICs, ASSPs, FPGAs

## Slide 24: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM9
1998
Intel Pentium 4
2000
Intel Pentium M
2003
ARM11
2002
ARM
Cortex - M
2004
ARM
Cortex - A
2005
ARM
Cortex - R
2011
Intel Quark
2013
Processors Timeline from 1990 to 2019

## Slide 25: Real-Time and Applications processors
 | Cortex-R7 | Cortex-A72
Cache | Data cache; Instruction cache. | Configurable Cache; L2: 512KB – 4MB; Instruction cache: 48 KB; Data cache: 32 KB.
Registers | No significant innovations; | No significant innovations;
Instructions | Thumb-2; SIMD and Vector Floating Point; | Thumb-2 and ThumbEE instruction sets; SIMD; Vector Floating Point optional.
Architecture | Dual Core; | Quad Core;
Notes: Cortex A La famiglia Cortex A è stata sviluppata al fine di ottenere prestazioni elevate e consumi ridotti. Indirizzata ai computer, telefoni cellulari evoluti e più in generale le applicazioni che necessitano di potenza di calcolo e flessibilità.
The ThumbEE instruction set is based on Thumb, with some changes and additions to make it a better target for dynamically generated code.

## Slide 26: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM9
1998
Intel
Pentium 4
2000
Intel Pentium M
2003
ARM11
2002
ARM
Cortex - M
2004
ARM
Cortex - A
2005
ARM
Cortex - R
2011
Intel Core i7
2008
Intel Core i5
2009
Intel Core i3
2010
Intel Quark
2013
Processors Timeline from 1990 to 2019

## Slide 27: The Intel Core family
 | Core i7 1st generation
Cache: | L1=4x64KB; L2=4x256KB; L3=8MB.
Instructions | Support: MMX; SSE 4.2.
Architecture | 4 core.
 | Core i5 1st generation
Cache: | L1=4x64KB; L2=4x256KB; L3=8MB-
Instructions | Support: MMX; SSE 4.2.
Architecture | 2 core.
 | Core i3 1st generation
Cache: | L1=2x64KB; L2=2x256KB; L3=4MB.
Instructions | Support: MMX; SSE 4.2.
Architecture | 2 core.
Notes: Core i7 brand targets the business and high-end consumer markets for both desktop and laptop computers,

## Slide 28: ARM & INTEL historical evolution
ARM3
1990
Intel Pentium
1993
ARM6
1991
Intel P6 Family
1995
ARM7
1994
ARM9
1998
Intel Pentium M
2003
ARM11
2002
ARM
Cortex - M
2004
ARM
Cortex - A
2005
ARM
Cortex - R
2011
Intel Core i7
2008
Intel Core i5
2009
Intel Core i5
2010
Intel Core i9
2017
ARM
Neoverse
Cores
2019
Intel Quark
2013
Processors Timeline from 1990 to 2019
Intel
Pentium 4
2000

## Slide 29: The new processors
ARM introduced the Neoverse cores at ARM TechCon 2018. The Neoverse N1 platform is the first computer platform from ARM capable of servicing the wider range of data center workloads with performance levels competitive with the legacy architectures used in the public cloud. ARM's platform provides a huge number of other advantages – diversity of business models, power efficiency enabling more performance at the edge, and higher performance system architectures (on-chip and off-chip).
Intel Core i9 brand microprocessors. They were introduced in May 2017.
With their high number of cores, high power draw, high thermal output, and high performance.
ARM Neoverse Cores
Intel Core i9

## Slide 30
Conclusion
Processors historical evolution summary
The present historical excursus shows how ARM and Intel processors have evolved during the years. The most exciting thing was to find out how two of the world-leading processors companies, like ARM and Intel, have improved their products increasing the processors speed-up.
Since the 1990s, the two companies have provided different kinds of functionalities to their processors to make them more and more powerful and meet the ever-growing market demand.
The results of these improvements lead the processors to become an essential member of human daily life.

## Slide 31: References
C. Cullinan, C. Wyant, T. Frattesi, and X. Huang, " Computing Performance Benchmarks among CPU, GPU, and FPGA " in high performance computing on graphics processing units: hgpu.org, April 2012.
A. Danowitz, K. Kelley, J. Mao, J. P. Stevenson and M. Horowitz "CPU DB: Recording Microprocessor History " in acmqueue, vol.10, Issue 4, April 2012.
J. V. Vijay, B. Bansode , ARM Processor Architecture Evolution and Applications, in International Journal of Science, Engineering and Technology Research (IJSETR), Vol. 4, Issue 10, Oct. 2015.
Markus Levy. The history of the ARM architecture: From inception to IPO. ARM IQ, 4(1), 2005.
I. Davey, P.Oliveri, The ARM11 Architecture, Spring 2009 CS433. https://www.cs.virginia.edu/~skadron/cs433_s09_processors/arm11.pdf. (Accessed: Oct. 2019).
Intel, Intel® 64 and IA-32 Architectures Software Developer’s Manual, vol: 1-4, 2019, Accessed: Sept. 2019. [Online]. Available: https://software.intel.com/sites/default/files/managed/39/c5/325462-sdm-vol-1-2abcd-3abcd.pdf.
Intel, P6 Family of Processors Hardware Developer’s Manual, Accessed: Nov. 2019. [Online]. Available: http://download.intel.com/design/PentiumII/manuals/24400101.pdf.
ARM, ARM Cortex-R Architecture, 2013, Accessed: Oct. 2019. [Online]. Available: https://www.arm.com/files/pdf/ARMv8R__Architecture_Oct13.pdf.
Intel 8088. https://it.wikipedia.org/wiki/Intel_8088. (Accessed: Oct. 2019).
Intel 8087. https://it.wikipedia.org/wiki/Intel_8087. (Accessed: Oct. 2019).

## Slide 32: References
Introduction to ARM processor. https://electronicsforu.com/resources/learn-electronics/introduction-arm-processor. (Accessed: Oct. 2019).
BBC Micro. https://it.wikipedia.org/wiki/BBC_Micro. (Accessed: Oct. 2019).
Home computer. https://it.wikipedia.org/wiki/Home_computer. (Accessed: Oct. 2019).
Acorn Computers. http://www.computinghistory.org.uk/det/897/Acorn-Computers/ (Accessed: Oct. 2019).
ARM. http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.set.arm11/index.html. (Accessed: Oct. 2019).
Pentium M. https://it.wikipedia.org/wiki/Pentium_M. (Accessed: Oct. 2019).
CPU-World. http://www.cpu-world.com/CPUs/Pentium_M/index.html. (Accessed: Oct. 2019).
ARM Community. https://community.arm.com/developer/ip-products/processors/b/processors-ip-blog/posts/a-brief-history-of-arm-part-1. (Accessed: Oct. 2019).
ARM architecture. https://en.wikipedia.org/wiki/ARM_architecture. (Accessed: Oct. 2019).
ARM6 - Microarchitectures – ARM. https://en.wikichip.org/wiki/arm_holdings/microarchitectures/arm6#Key_changes_from_ARM3. (Accessed: Oct. 2019).
List of ARM microarchitectures. https://en.wikipedia.org/wiki/List_of_ARM_microarchitectures#ARM_core_timeline. (Accessed: Oct. 2019).

## Slide 33: References
Computer processor history. https://www.computerhope.com/history/processor.htm. (Accessed: Nov. 2019).
The History of the CPU. https://www.preceden.com/timelines/239458-the-history-of-the-cpu. (Accessed: Nov. 2019)
Pentium. https://encyclopedia2.thefreedictionary.com/80586. (Accessed: Nov. 2019)
Pentium Pro Architecture. https://www.geeksforgeeks.org/pentium-pro-architecture/. (Accessed: Nov. 2019)
Intel Pentium II Xeon microprocessor family. http://www.cpu-world.com/CPUs/Pentium-II/TYPE-Pentium%20II%20Xeon.html (Accessed: Nov. 2019)
IFEL ARM3 36MHz processor upgrade . https://www.retro-kit.co.uk/page.cfm/content/IFEL-ARM3-36MHz-processor-upgrade/. (Accessed: Nov. 2019)

## Slide 34
THANK YOU!
Gabriella D’Andrea - gabriella.dandrea@graduate.univaq.it